## Slide 1: Pouch Stacker & Boxer DR-86249 Mark Smith October 8, 2015

## Slide 2: Pouch Stacker & Boxer DR-86249 10/8/15
Ergonomics
Legs Added
Pouch boxing area now w/i easy reach.
Leg Lockdowns added to secure Legs to table.
Locks are universal: good for any round legs Ø.750 to Ø2.000.
Mounting holes in Base for rubber feet if Legs are removed.

## Slide 3: Pouch Stacker & Boxer DR-86249 10/8/15
Parts Counter
Flexibility Added: Sensor & Reflector can be mounted in either location.

## Slide 4: Pouch Stacker & Boxer DR-86249 10/8/15
Platform
Easily adjustable to suit length of Pouch.
Reflector Mount & Platform easily removable to access front panel door of Sealer machine.

## Slide 5: Pouch Stacker & Boxer DR-86249 10/8/15
Short Legs
Positively locates & secures Pouch Sealer machine.
Allows room for electronic cables etc. to pass under the machine as needed.

## Slide 6: Pouch Stacker & Boxer DR-86249 10/8/15
Angled Chute
Adjustable to allow for changes in Pouch length and/or machine depth settings.
High walls to better guide the Pouches in their descent.

## Slide 7: Pouch Stacker & Boxer DR-86249 10/8/15
The Lock Handle also functions to pull the Pouch Stacker to the Box area.
Long Handle is easily within reach of operator.
The Lids prevent debris entrance, and are two of the same part, to reduce costs.
The Lids can also be installed/removed without removing the Axel.
Lock Ramp position can be adjusted, and reversed if/when one ramp wears out.

## Slide 8: Pouch Stacker & Boxer DR-86249 10/8/15
Pouch Stacker rides on Delrin glides.
The Axel lifts up & out of its groove in the Indexing Base to rotate, indexing 180°.
Both of the above parts are aluminum with hard anodize, to reduce costs.
Both parts are simple to machine.

## Slide 9: Pouch Stacker & Boxer DR-86249 10/8/15
These Adjustable Stops can be oriented at 0° to 90°.
Rubber Bumpers can be attached to any face.
The Stops are universal- can be used in other projects.

## Slide 10: Pouch Stacker & Boxer DR-86249 10/8/15
Location of Entire Pouch stacking area is adjustable to account for variations in Pouch egress from the Sealer machine.

## Slide 11: Pouch Stacker & Boxer DR-86249 10/8/15
Heavy Duty
Heavy duty sheet metal Angle Brace, designed for universal usage spanning many different projects, helps to reinforce the 1” thick aluminum Stacker Sliding Plate.

## Slide 12: Pouch Stacker & Boxer DR-86249 10/8/15
Pouch Stacker
Comfortable Grab Handles to pull the Pouch Stacker to the boxing area.
Grab Handles double as framework/guides for the Sliding Door (not shown).
Easy hand access to pick up and push/guide Pouches towards Box.
Sturdy reinforcements to prevent twisting, bending.

## Slide 13: Pouch Stacker & Boxer DR-86249 10/8/15
Door & Door Frame
Door Stop prevents Sliding Door from going too far in, too far out.
Door has an easy grab handle for the operator to pull it open.
Door Frame also doubles as a “funnel” to initiate the guidance of the Pouches into their awaiting Box.

## Slide 14: Pouch Stacker & Boxer DR-86249 10/8/15
Pouch Stacker Posts
Cheap aluminum barstock makes up the 11 Posts that guide the Pouches in.
Posts are tapered with a leading angle & spaced far enough apart to account for the up to ± ¼” potential difference in Pouch size.

## Slide 15: Pouch Stacker & Boxer DR-86249 10/8/15
Pouch Stacker Posts
Cheap aluminum barstock makes up the 11 Posts that guide the Pouches in.
Posts are tapered with a leading angle & spaced far enough apart to account for the up to ± ¼” potential difference in Pouch size.

## Slide 16: Pouch Stacker & Boxer DR-86249 10/8/15
Boxing Process
Clear Lexan guide walls allow visual confirmation as they funnel the Pouches into the Box.
Large hand access cutouts in the Door Frame & Lexan Guide Roof allows the operator to continue pushing the Pouches almost all the way into the Box opening itself.
Two .015” thick stainless steel shims keep the “roof” of the Box open during loading.

## Slide 17: Pouch Stacker & Boxer DR-86249 10/8/15
Boxing Process
The main flap of the Box is secured underneath & out of the way.
Having mechanically secured all three flaps & the “roof” of the Box, the Pouches will now slid easily into the Box.
All that remains is for the operator to remove the box and lightly tamp down the Pouches.

## Slide 18: Pouch Stacker & Boxer DR-86249 10/8/15